## Slide 1
Antigoni Kleanthous, University College London, UK
Timo Betcke, University College London, UK
David Hewett, University College London, UK
Anthony Baran, The Met Office, UK & University of Hertfordshire, UK
Latest BEM developments
and
The microwave and sub-millimetre database
December 2020

## Slide 2
Part I: Accelerated Calderón preconditioning for Maxwell transmission problems
Antigoni Kleanthous, University College London, UK
Timo Betcke, University College London, UK
David Hewett, University College London, UK
Paul Escapil-Inchauspé, Universidad Adolfo Ibáñez, Santiago, Chile
Carlos Jerez-Hanckes, Pontificia Universidad Católica de Chile, Santiago, Chile
Anthony Baran, The Met Office, UK & University of Hertfordshire, UK

## Slide 3: The Boundary Element Method (BEM)
Reformulate the problem into boundary integral equations on the boundary of the scatterer
Discretise the boundary and transform the boundary integral equations into a matrix system
Solve the discrete problem on the boundary using an iterative solver
The solution on the boundary can be extended to the interior/exterior/far field area through representation formulae

## Slide 4: Why use BEM?
Reduces the dimensionality of the problem from a 3D domain to a 2D manifold
  Discretisation is easier/faster
  The matrix system is smaller
Radiation conditions at infinity automatically satisfied
Can solve the full time-harmonic Maxwell problem without the need for any approximations
Can handle complicated domains – ideal for complex shaped ice crystals

## Slide 6: The scattering problem

## Slide 7: The scattering problem

## Slide 8: The scattering problem

## Slide 9: The PMCHWT formulation

## Slide 10: Calderón Preconditioning

## Slide 11: Accelerated Preconditioning
To accurately capture the wave solution a mesh refinement of 10 elements per wavelength is usually used
To stably discretise the operator product PA, the use of a dual mesh is required. The dual mesh is defined on the barycentrically refined original mesh leading to a 6-fold increase in the number of elements
Applications have been limited to relatively small size parameters due to memory and time constraints.
Accelerating techniques to reduce memory and assembly time

## Slide 12: Accelerated Preconditioning
To accurately capture the wave solution a mesh refinement of 10 elements per wavelength is usually used
To stably discretise the operator product PA, the use of a dual mesh is required. The dual mesh is defined on the barycentrically refined original mesh leading to a 6-fold increase in the number of elements
Applications have been limited to relatively small size parameters due to memory and time constraints.
Accelerating techniques to reduce memory and assembly time

## Slide 13: Accelerated Preconditioning
To accurately capture the wave solution a mesh refinement of 10 elements per wavelength is usually used
To stably discretise the operator product PA, the use of a dual mesh is required. The dual mesh is defined on the barycentrically refined original mesh leading to a 6-fold increase in the number of elements
Applications have been limited to relatively small size parameters due to memory and time constraints.
Accelerating techniques to reduce memory and assembly time

## Slide 14: Accelerated Preconditioning

## Slide 15: Accelerated Preconditioning: operator-based approach
Goal: Reduce number of operators used in the preconditioner
A reduced preconditioner has a weakened preconditioning effect – balance between memory/assembly time savings and solver time

## Slide 17: Accelerated Preconditioning: implementation
Use a relaxed set of parameters for the preconditioner; the preconditioner is used to accelerate solution time – accuracy is not affected

## Slide 19: Accelerated Preconditioning

## Slide 20: Accelerated Preconditioning – 50GHz

## Slide 21: Accelerated Preconditioning – 183GHz

## Slide 22: Accelerated Preconditioning – 325GHz

## Slide 23: Accelerated Preconditioning – 664GHz
Unable to assemble the matrices except for Sibp
Assembly time:
  10 minutes for the preconditioner
  32 minutes for the operator
GMRES time:
  62 minutes
  166 iterations
Memory:
  9GB for preconditioner – estimated to be ~1-2% of the original non-accelerated version
  109GB for operator

## Slide 25
Part II: Using accelerated BEM for a microwave and sub-millimetre database
Antigoni Kleanthous, University College London, UK
Timo Betcke, University College London, UK
David Hewett, University College London, UK
Anthony Baran, The Met Office, UK & University of Hertfordshire, UK
Chris Westbrook, University of Reading, UK

## Slide 26: The database
Goal: simulate SSPs and phase matrices of budding rosettes and aggregates of bullet rosettes in random orientation
5 temperatures: 190K, 210K, 230K, 250K, 270K
4 frequencies: 50GHz, 183GHz, 243GHz and 664GHz
Range of sizes from μm to cm

## Slide 27: The microphysical model
Notes: analysis of more than 100 images from Cloud Particle Imager (CPI) data from twenty-two campaigns distributed throughout the mid-latitudes, tropics, and southern latitudes

## Slide 28: The microphysical model
Notes: From that analysis, the most representative ice crystal shapes of relevance to modelling millimetre wave and sub-millimetre wave scattering within in-situ generated cirrus (prevalent in the mid-latitudes) are budding rosettes and aggregates of rosettes, which we use to generate our ensemble model.

## Slide 29: The microphysical model
The aggregates were generated using the ice aggregation model of (Westbrook, et al., 2004) formed by Monte Carlo simulations
The monomer rosettes are constructed of three-branched rosettes, which are aggregated together to follow the Cotton et al. mass–dimension relationship – to be consistent with the Unified Model used at the Met Office
Each of the monomers that makes up the ensemble of rosette aggregates is assumed to have the density of solid ice, 917 kg/m3
The final model consists of 65 aggregates, of maximum dimension between 10 and 10,000μm.

## Slide 30: The microphysical model
Notes: At sizes between 10-492 μm the rosette aggregate is scaled, and so is invariant with respect to its maximum dimension up until 492 μm. The remaining aggregates are all different as they are from different realisations of the Monte Carlo simulations. The aggregates consist of 6 to 168 monomers of different complexity.

## Slide 31: The microphysical model

## Slide 32: The microphysical model

## Slide 33: The microphysical model

## Slide 34: Simulating random orientation
The orientation average of some quantity is evaluated by a triple integral over the three Euler angles used to describe the orientation of a body
The traditional approach to achieve this is to fix the direction of the incident wave, and then rotate the particle in three directions via the three Euler angles. The SSPs and phase matrix are then evaluated for some scattering angles.

## Slide 35: Simulating random orientation
The traditional approach would be too expensive to follow using BEM: each rotation requires the assembly of a new matrix operator and preconditioner.
Fixing the direction of the incident wave and rotating the scatterer by the appropriate rotation matrix is equivalent to fixing the orientation of the scatterer and instead rotating the direction and polarisation vectors of the incident wave by the inverse rotation matrix.
This enables us to assemble the operator matrix and preconditioner once and re-use for all incident wave solutions. By using appropriate quadrature schemes suitable for numerical integration over a sphere our integration scheme reduces to only 2 loops; a combination of Lebedev and Gaussian quadrature.
In addition, the different incoming waves are distributed over different CPUs to accelerate solution even further.

## Slide 36: Testing our method
Notes: Solid lines: refined mesh

## Slide 37: Testing our method – X=0.05
Notes: X=0.05
Mesh of 100 elements per wavelength
6 incident waves
5 rotations of the polarisation vectors

## Slide 38: Testing our method – X=1
Notes: X=1
14 incident waves
10 rotations of the polarisation vectors

## Slide 39: Testing our method – X=5
Notes: X=5
110 incident waves
10 rotations of the polarisation vectors

## Slide 40: Testing our method – X=10
Notes: X=10
194 incident waves
15 rotations of the polarisation vectors

## Slide 41: Testing our method
To obtain SSPs to within accuracies of 10% or so, (Liu, et al., 2008), using the discrete dipole approximation (DDA), found that 17 x 16 x 16 (4352) orientations were required to simulate random orientation.
With our method we can reduce the number of incident waves and rotations of the polarisation vectors needed depending on the size parameter of the aggregate.
To accurately compute the SSPs within accuracy of 1-5% we need
  X<1: 14 incident directions
  1<X<3: 50 incident waves
  3<X<5: 110 incident waves
  5<X<8: 194 incident waves
  8<X<10: 230 incident waves
  X>10: 302 incident waves
To obtain the phase matrix to 1-2% relative error we also need:
  X<1: 10 rotations of the polarisation vectors
  1<X<24: 15 rotations of the polarisation vectors
  X>24: 20 rotations of the polarisation vectors

## Slide 42
Part III: Scattering by inhomogeneous particles
Antigoni Kleanthous, University College London, UK
Timo Betcke, University College London, UK
David Hewett, University College London, UK
Anthony Baran, The Met Office, UK & University of Hertfordshire, UK

## Slide 43: Inhomogeneous scatterers
The boundary integral formulation and preconditioning can be easily extended to simulate scattering by inhomogeneous scatterers
  Hexagonal columns with air bubbles
  Ice crystal in a liquid droplet
Notes: - Inhomogeneous Hexagonal monocrystal
– ice crystals falling through the atmosphere

## Slide 44
Notes: 8-branch aggregate in a liquid sphere, 50GHz

## Slide 45: Future Steps
Complete simulations for the database to include phase matrix calculations
Time permitting, explore scattering by inhomogeneous scatterers